## Slide 1
Computer Organization and Architecture
Prof. Indranil Sengupta
Dr. Sarani Bhattacharya
Department of Computer Science and Engineering
IIT Kharagpur

## Slide 2
MIPS32 INSTRUCTION SET

## Slide 3: Instruction Set Classification
MIPS32 instruction can be classified into the following functional groups:
  Load and Store
  Arithmetic and Logical
  Jump and Branch
  Miscellaneous
  Coprocessor instruction (to activate an auxiliary processor).
All instructions are encoded in 32 bits.

## Slide 4: Alignment of Words in Memory
MIPS requires that all words must be aligned in memory to word boundaries.
  Must start from an address that is some power of 4.
  Last two bits of the address must be 00.
Allows a word to be fetched in a single cycle.
  Misaligned words may require two cycles.
w1
w1
w1
w1
w2
w2
w2
w2
w3
w3
w3
w3
w4
w4
w4
w4
0000H
0004H
0008H
000CH
0010H
0014H
0018H
Address
w1 is aligned, but w2, w3, w4 are not

## Slide 5: (a) Load and Store Instructions
MIPS32 is a load-store architecture.
  All operations are performed on operands held in processor registers.
  Main memory is accessed only through LOAD and STORE instructions.
There are various types of LOAD and STORE instructions, each used for a particular purpose.
  By specifying the size of the operand (W: word, H: half-word, B: byte)
    Examples: LW, LH, LB, SW, SW, SB
  By specifying whether the operand is signed (by default) or unsigned.
    Examples: LHU, LBU

## Slide 6
  Accessing fields that are not word aligned.
    Examples: LWL, LWR, SWL, SWR
  Atomic memory update for read-modify-write instructions
    Examples: LL, SC

## Slide 7
Data Size | Load Signed | Load Unsigned | Store
Byte | YES | YES | YES
Half-word | YES | YES | YES
Word | YES | Only for MIPS64 | YES
Unaligned word | YES |  | YES
Linked word (atomic modify) | YES |  | YES
Data sizes that can be accessed through LOAD and STORE

## Slide 8
Type | Mnemonic | Function
Aligned | LB | Load Byte
 | LBU | Load Byte Unsigned
 | LH | Load Half-word
 | LHU | Load Half-word Unsigned
 | LW | Load Word
 | SB | Store Byte
 | SH | Store Half-word
 | SW | Store Word
Type | Mnemonic | Function
Unaligned | LWL | Load Word Left
 | LWR | Load Word Right
 | SWL | Store Word Left
 | SWR | Store Word Right
Atomic Update | LL | Load Linked Word
 | SB | Store Conditional Word

## Slide 9: (b) Arithmetic and Logic Instructions
All arithmetic and logic instructions operate on registers.
Can be broadly classified into the following categories:
  ALU immediate
  ALU 3-operand
  ALU 2-operand
  Shift
  Multiply and Divide

## Slide 10
Type | Mnemonic | Function
16-bit Immediate Operand | ADDI | Add Immediate Word
 | ADDIU | Add Immediate Unsigned Word
 | ANDI | AND Immediate
 | LUI | Load Upper Immediate
 | ORI | OR Immediate
 | SLTI | Set on Less Than Immediate
 | SLTIU | Set on Less Than Immediate Unsigned
 | XORI | Exclusive-OR Immediate

## Slide 11
Type | Mnemonic | Function
3-Operand | ADD | Add Word
 | ADDU | Add Unsigned Word
 | AND | Logical AND
 | NOR | Logical NOR
 | SLT | Set on Less Than
 | SLTU | Set on Less Than Unsigned
 | SUB | Subtract Word
 | SUBU | Subtract Unsigned Word
 | XOR | Logical XOR

## Slide 12
Type | Mnemonic | Function
Shift | ROTR | Rotate Word Right
 | ROTRV | Rotate Word Right Value (Register)
 | SLL | Shift Word Left Logical
 | SLLV | Shift Word Left Logical Value (Register)
 | SRA | Shift Word Right Arithmetic
 | SRAV | Shift Word Right Arithmetic Value (Register)
 | SRL | Shift Word Right Logical
 | SRLV | Shift Word Right Logical Value (Register)

## Slide 13: (c) Multiply and Divide Instructions
The multiply and divide instructions produce twice as many result bits.
  When two 32-bit numbers are multiplied, we get a 64-bit product.
  After division, we get a 32-bit quotient and a 32-bit remainder.
Results are produced in the HI and LO register pair.
  For multiplication, the low half of the product is loaded into LO, while the higher half in HI.
  Multiply-Add and Multiply-Subtract produce a 64-bit product, and adds or subtracts the product from the concatenated value of HI and LO.
  Divide produces a quotient that is loaded into LO and a remainder that is loaded into HI.

## Slide 14
Only exception is the MUL instruction, which delivers the lower half of the result directly to a GPR.
  Useful is situations where the product is expected to fit in 32 bits.

## Slide 15
Type | Mnemonic | Function
Multiply and Divide | DIV | Divide Word
 | DIVU | Divide Unsigned Word
 | MADD | Multiply and Add Word
 | MADDU | Multiply and Add Word Unsigned
 | MFHI | Move from HI
 | MFLO | Move from LO
 | MSUB | Multiply and Subtract Word
 | MSUBU | Multiply and Subtract Word Unsigned
 | MTHI | Move to HI
 | MTLO | Move to LO
 | MUL | Multiply Word to Register
 | MULT | Multiply Word
 | MULTU | Multiply Unsigned Word

## Slide 16: (d) Jump and Branch Instructions
The following types of Jump and Branch instructions are supported by MIPS32.
  PC relative conditional branch
    A 16-bit offset is added to PC.
  PC-relative unconditional jump
    A 28-bit offset if added to PC.
  Absolute (register) unconditional jump
  Special Jump instructions that link the return address in R31.

## Slide 17
Type | Mnemonic | Function
Unconditional Jump within a 256 MB Region | J | Jump
 | JAL | Jump and Link
 | JALX | Jump and Link Exchange
Type | Mnemonic | Function
Unconditional Jump using Absolute Address | JALR | Jump and Link Register
 | JR | Jump Register

## Slide 18
Type | Mnemonic | Function
PC-Relative Conditional Branch Comparing Two Registers | BEQ | Branch on Equal
 | BNE | Branch on Not Equal
Type | Mnemonic | Function
PC-Relative Conditional Branch Comparing With Zero | BGEZ | Branch on Greater Than or Equal to Zero
 | BGEZAL | Branch on Greater Than or Equal to Zero and Link
 | BGTZ | Branch on Greater than Zero
 | BLEZ | Branch on Less Than or Equal to Zero

## Slide 19: (e) Miscellaneous Instructions
These instructions are used for various specific machine control purposes.
They include:
  Exception instructions
  Conditional MOVE instructions
  Prefetch instructions
  NOP instructions

## Slide 20
Type | Mnemonic | Function
System Call and Breakpoint | BREAK | Breakpoint
 | SYSCALL | System Call
Type | Mnemonic | Function
Trap-on-Condition Comparing Two Registers | TEQ | Trap in Equal
 | TGE | Trap if Greater Than or Equal
 | TGEU | Trap if Greater Than or Equal Unsigned
 | TLT | Trap if Less Than
 | TLTU | Trap if Less Than Unsigned
 | TNE | Trap if Not Equal
Type | Mnemonic | Function
Trap-on-Condition Comparing an Immediate Value | TEQI | Trap if Equal Immediate
 | TGEI | Trap if Greater Than or Equal Immediate
 | TGEIU | Trap if Greater Than or Equal Immediate Unsigned
 | TLTI | Trap if Less Than Immediate
 | TLTIU | Trap if Less Than Immediate Unsigned
 | TNEI | Trap if Not Equal Immediate

## Slide 21
Type | Mnemonic | Function
Conditional Move | MOVF | Move Conditional on Floating Point False
 | MOVN | Move Conditional on Not Zero
 | MOVT | Move Conditional on Floating Point True
 | MOVZ | Move Conditional on Zero
Type | Mnemonic | Function
Prefetch | PREF | Prefetch Register+Offset
NOP | NOP | No Operation

## Slide 22: (e) Coprocessor Instructions
The MIPS architecture defines four coprocessors (designated CP0, CP1, CP2, and CP3).
  Coprocessor 0 (CP0) is incorporated on the CPU chip and supports the virtual memory system and exception handling. CP0 is also referred to as the System Control Coprocessor.
  Coprocessor 1 (CP1) is reserved for the floating point coprocessor.
  Coprocessor 2 (CP2) is available for specific implementations.
  Coprocessor 3 (CP3) is available for future extensions.
These instructions are not discussed here.

## Slide 23
MIPS32 architecture also supports a set of floating-point registers and floating-point instructions.
  Shall be discussed later.

## Slide 24
MIPS PROGRAMMING EXAMPLES

## Slide 25: Some Examples of MIPS32 Arithmetic
A = B + C;
C Code
add $s1, $s2, $s3
MIPS32 Code
A = B + C – D;
E = F + A;
C Code
add $t0, $s1, $s2
sub $s0, $t0, $s3
add $s4, $s5, $s0;
MIPS32 Code
B loaded in $s2
C loaded in $s3
A  $s1
B loaded in $s1
C loaded in $s2
D loaded in $s3
F loaded in $s5
$t0 is a temporary
A  $s0; E  $s4

## Slide 26: Example on LOAD and STORE
A[10] = X – A[12];
C Code
lw $t0, 48($s3)
sub $t0, $s2, $t0
sw $t0, 40($s3);
MIPS32 Code
$s3 contains the starting address of the array A
$s2 loaded with X
$t0 is a temporary
Address of A[10] will be $s3+40 (4 bytes per element)
Address of A[12] will be $s3+48

## Slide 27: Examples on Control Constructs
if (x==y) z = x – y;
C Code
bne $s0, $s1, Label
sub $s3, $s0, $s1
Label: ……
MIPS32 Code
$s0 loaded with x
$s1 loaded with y
z  $s3

## Slide 28
if (x != y) z = x – y;
else z = x + y;
C Code
beq $s0, $s1, Lab1
sub $s3, $s0, $s1
j Lab2
Lab1: add $s3, $s0, $s1
Lab2: ….
MIPS32 Code
$s0 loaded with x
$s1 loaded with y
z  $s3

## Slide 29
MIPS32 supports a limited set of conditional branch instructions:
  beq $s2,Label // Branch to Label of $s2 = 0
  bne $s2,Label // Branch to Label of $s2 != 0
Suppose we need to implement a conditional branch after comparing two registers for less-than or greater than.
if (x < y) z = x – y;
else z = x + y;
C Code
slt $t0,$s0,$s1
beq $t0, $zero, Lab1
sub $s3, $s0, $s1
j Lab2
Lab1: add $s3, $s0, $s1
Lab2: ….
MIPS32 Code
Set if less than.
If $s0 < $s1, then set $t0=1; else $t0=0.

## Slide 30
MIPS32 assemblers supports several pseudo-instructions that are meant for user convenience.
  Internally the assembler converts them to valid MIPS32 instructions.
Example: The pseudo-instruction branch if less than
blt $s1, $s2, Label
slt $at, $s1, $s2
bne $t0, $zero, Label
….
Label: ….
MIPS32 Code
The assembler requires an extra register to do this.
The register $at (= R1) is reserved for this purpose.

## Slide 31: Working with Immediate Values in Registers
Case 1: Small constants, which can be specified in 16 bits.
  Occurs most frequently (about 90% of the time).
  Examples:
    A = A + 16;  addi $s1, $s1, 16 (A in $s1)
    X = Y – 1025;  subi $s1, $s2, 1025 (X in $s1, Y in $s2)
    A = 100;  addi $s1, $zero, 100 (A in $s1)

## Slide 32
Case 2: Large constants, that require 32 bits to represent.
  How to load a large constant in a register?
  Requires two instructions.
    A “Load Upper Immediate” instruction, that loads a 16-bit number into the upper half of a register (lower bits filled with zeros).
    An “OR Immediate” instruction, to insert the lower 16-bits.
  Suppose we want to load 0xAAAA3333 into a register $s1.
lui $s1, 0xAAAA
ori $s1, $s1, 0x3333
1010101010101010
0000000000000000
1010101010101010
0011001100110011

## Slide 33: Other MIPS Pseudo-instructions
Pseudo-Instruction | Translates to | Function
blt $1, $2, Label | slt $at, $1, $2 bne $at, $zero, Label | Branch if less than
bgt $1, $2, Label | sgt $at, $1, $2 bne $at, $zero, Label | Branch if greater than
ble $1, $2, Label | sle $at, $1, $2 bne $at, $zero, Label | Branch if less or equal
bge $1, $2, Label | sge $at, $1, $2 bne $at, $zero, Label | Branch if greater or equal
li $1, 0x23ABCD | lui $1, 0x0023 ori $1, $1, 0xABCD | Load immediate value into a register

## Slide 34
Pseudo-Instruction | Translates to | Function
move $1, $2 | add $1, $2, $zero | Move content of one register to another
la $a0, 0x2B09D5 | lui $a0, 0x002B ori $a0, $a0, l0x09D5 | Load address into a register

## Slide 35: A Simple Function
swap (int A[], int k)
{
int temp;
temp = A[k];
A[k] = A[k+1];
A[k+1] = temp;
}
C Function
Exchange A[k] and A[k+1]
swap: muli $t0, $s0, 4
add $t0, $s1, $t0
lw $t1, 0($t0)
lw $t2, 4($t0)
sw $t2, 0($t0)
sw $t1, 4($t0)
jr $ra
MIPS32 Code
$s0 loaded with index k
$s1 loaded with base address of A
Address of A[k] = $s1 + 4 * $s0

## Slide 36: MIPS Instruction Encoding
All MIPS32 instructions can be classified into three groups in terms of instruction encoding.
  R-type (Register), I-type (Immediate), and J-type (Jump).
  In an instruction encoding, the 32 bits of the instruction are divided into several fields of fixed widths.
  All instructions may not use all the fields.
Since the relative positions of some of the fields are same across instructions, instruction decoding becomes very simple.

## Slide 37: (a) R-type Instruction Encoding
Here an instruction can use up to three register operands.
  Two source and one destination.
In addition, for shift instructions, the number of bits to shift can also be specified.
opcode
rs
rd
rt
shamt
funct
0
16
15
11
10
6
5
31
26
25
21
20
6-bit opcode
Source register 1
Source register 2
Destination register
Shift amount
Opcode extension (additional functions)

## Slide 38
Examples of R-type instructions:
  add $s1, $s2, $s3
  sub $t1, $s3, $s4
  sll $s1, $s2, 5 // shift left $s2 by 5 places, and store in $s1
  An example instruction encoding: add $t1, $s1, $s2
    Recall: $t1 is R9, $s1 is R17, and $s2 is R18.
    For “add”, opcode = 000000, and funct = 100000,
000000
10001
01001
10010
00000
100000
0
16
15
11
10
6
5
31
26
25
21
20

## Slide 39: (b) I-type Instruction Encoding
Contains a 16-bit immediate data field.
Supports one source and one destination register.
opcode
rs
Immediate Data
rt
0
16
15
31
26
25
21
20
6-bit opcode
Source register 1
Destinationregister
16-bit immediate data

## Slide 40
Examples of I-type instructions:
  lw $s1, 50($s5)
  sw $t1, 100($s1)
  addi $t0, $s1, 188
  beq $s1, $s2, Label // Label is encoded as a 16-bit offset relative to PC
  bne $s3, $zero, Label
  An example instruction encoding: lw $t1, 48($s1)
    Recall: $t1 is R9, $s1 is R17.
    For “lw”, opcode = 100011.
100011
10001
01001
0000000000110000
0
16
15
31
26
25
21
20

## Slide 41: (c) J-type Instruction Encoding
Contains a 26-bit jump address field.
  Extended to 28 bits by padding two 0’s on the right.
Example: j Label
opcode
Immediate Data
0
31
26
25
6-bit opcode
26-bit jump address

## Slide 42: A Quick View
opcode
rs
Immediate Data
rt
0
16
15
31
26
25
21
20
opcode
rs
rd
rt
shamt
funct
0
16
15
11
10
6
5
31
26
25
21
20
opcode
Immediate Data
0
31
26
25
R-type
I-type
J-type
Some instructions require two register operands rs & rt as input, while some require only rs.
Gets known only after instruction is decoded.
While decoding is going on, we can prefetch the registers in parallel.
  May or may not be required later.
Similarly, the 16-bit and 26-bit immediate data are retrieved and sign-extended to 32-bits in case they are required later.

## Slide 43: Addressing Modes in MIPS32
Register addressing add $s1, $s2, $s3
Immediate addressing addi $s1, $s2, 200
Base addressing lw $s1, 150($s2)
  Content of a register is added to a “base” value to get the operand address.
PC relative addressing beq $s1, $s2, Label
  16-bit offset is added to PC to get the target address.
Pseudo-direct addressing j Label
  26-bit offset if shifted left by 2 bits and then added to PC to get the target address.

## Slide 44
AMDAHL’S LAW

## Slide 45: Introduction
Gene Amdahl
Amdahl’s law was established in 1967 by Gene Amdahl.
Basically provides an understanding on scaling, limitations and economics of parallel computing.
Forms the basis for quantitative principles in computer system design.
  Can be applied to other application domains as well.

## Slide 46: What is Amdahl’s Law?
It can be used to find the maximum expected improvement of an overall system when only part of the system is improved.
It basically states that the performance improvement to be gained from using some faster mode of execution is limited by the fraction of the time the faster mode can be used.
Very useful to check whether any proposed improvement can provide expected return.
  Used by computer designers to enhance only those architectural features that result in reasonable performance improvement.
  Referred to as quantitative principles in design.

## Slide 47
Amdahl’s law demonstrates the law of diminishing returns.
An example:
  Suppose we are improving a part of the computer system that affects only 25% of the overall task.
  The improvement can be very little or extremely large.
  With “infinite” speedup, the 25% of the task can be done in “zero” time.
  Maximum possible speedup = XTorig / XTnew = 1 / (1 – 0.25) = 1.33
We can never get a speedup of more than 1.33

## Slide 48
Amdahl’s law concerns the speedup achievable from an improvement in computation that affects a fraction F of the computation, where the improvement has a speedup of S.
1 – F
F
1 – F
F / S
Before improvement
After improvement

## Slide 49
Speedup =
Execution time before improvement: (1 – F) + F = 1
Execution time after improvement: (1 – F) + F / S
Speedup obtained:
1
(1 – F) + F / S
As S  ∞, Speedup  1 / (1 – F)
  The fraction F limits the maximum speedup that can be obtained.

## Slide 50
Illustration of law of diminishing returns:
  Let F = 0.25.
  The table shows the speedup (= 1 / (1 – F + F / S) for various values of S.
S | Speedup
1 | 1.00
2 | 1.14
5 | 1.25
10 | 1.29
S | Speedup
50 | 1.32
100 | 1.33
1000 | 1.33
100,000 | 1.33
1 / (1 – 0.25) = 1.33

## Slide 51
Illustration of law of diminishing returns:
  Let F = 0.75.
  The table shows the speedup for various values of S.
S | Speedup
1 | 1.00
2 | 1.60
5 | 2.50
10 | 3.08
S | Speedup
50 | 3.77
100 | 3.88
1000 | 3.99
100,000 | 4.00
1 / (1 – 0.75) = 4.00

## Slide 52: Design Alternative using Amdahl’s law
Loop 1
Loop 2
500 lines
20 lines
10% of total execution time
90% of total execution time

## Slide 53
Some examples:
  We make 10% of a program 90X faster, speedup = 1 / (0.9 + 0.1 / 90) = 1.11
  We make 90% of a program 10X faster, speedup = 1 / (0.1 + 0.9 / 10) = 5.26
  We make 25% of a program 25X faster, speedup = 1 / (0.75 + 0.25 / 25) = 1.32
  We make 50% of a program 20X faster, speedup = 1 / (0.5 + 0.5 / 20) = 1.90
  We make 90% of a program 50X faster, speedup = 1 / (0.1 + 0.9 / 50) = 8.47

## Slide 54: Example 1
Suppose we are running a set of programs on a RISC processor, for which the following instruction mix is observed:
We carry out a design enhancement by which the CPI of Load instructions reduces from 5 to 2. What will be the overall performance improvement?
Operation | Frequency | CPIi
Load | 20 % | 5
Store | 8 % | 3
ALU | 60 % | 1
Branch | 12 % | 2
Wi * CPIi | % Time
1.00 | 0.48
0.24 | 0.12
0.60 | 0.29
0.24 | 0.11
CPI = 2.08
1 / 2.08

## Slide 55
Fraction enhanced F = 0.48
Fraction unaffected 1 – F = 1 – 0.48 = 0.52
Enhancement factor S = 5 / 2 = 2.5
Therefore, speedup is
1 1
(1 – F) + F / S 0.52 + 0.48 / 2.5
= 1.40
=

## Slide 56
Alternate way of calculation:
  Old CPI = 2.08
  New CPI = 0.20 * 2 + 0.08 * 3 + 0.60 * 1 + 0.12 * 2 = 1.48

## Slide 57: Example 2
The execution time of a program on a machine is found to be 50 seconds, out of which 42 seconds is consumed by multiply operations. It is required to make the program run 5 times faster. By how much must the speed of the multiplier be improved?
  Here, F = 42 / 50 = 0.84
  According to Amdahl’s law,
  5 = 1 / (0.16 + 0.84 / S)
  or, 0.80 + 4.2 / S = 1
  or, S = 21

## Slide 58: Example 2a
The execution time of a program on a machine is found to be 50 seconds, out of which 42 seconds is consumed by multiply operations. It is required to make the program run 8 times faster. By how much must the speed of the multiplier be improved?
  Here, F = 42 / 50 = 0.84
  According to Amdahl’s law,
  8 = 1 / (0.16 + 0.84 / S)
  or, 1.28 + 6.72 / S = 1
  or, S = – 24
No amount to speed improvement in the multiplier can achieve this.
Maximum speedup achievable:
1 / (1 – F) = 6.25

## Slide 59: Example 3
Suppose we plan to upgrade the processor of a web server. The CPU is 30 times faster on search queries than the old processor. The old processor is busy with search queries 80% of the time. Estimate the speedup obtained by the upgrade.
  Here, F = 0.80 and S = 30
  Thus, speedup = 1 / (0.20 + 0.80 / 30) = 4.41

## Slide 60: Example 4
The total execution time of a typical program is made up of 60% of CPU time and 40% of I/O time. Which of the following alternatives is better?
  Increase the CPU speed by 50%
  Reduce the I/O time by half
Assume that there is no overlap between CPU and I/O operations.
CPU
CPU
CPU
I/O
I/O
I/O

## Slide 61
Increase CPU speed by 50%
  Here, F = 0.60 and S = 1.5
  Speedup = 1 / (0.40 + 0.60 / 1.5) = 1.25
Reduce the I/O time by half
  Here, F = 0.40 and S = 2
  Speedup = 1 / (0.60 + 0.40 / 2) = 1.25
Thus, both the alternatives result in the same speedup.

## Slide 62: Example 5
Suppose that a compute-intensive bioinformatics program is running on a given machine X, which takes 10 days to run. The program spends 25% of its time doing integer instructions, and 40% of time doing I/O. Which of the following two alternatives provides a better tradeoff?
  Use an optimizing compiler that reduces the number of integer instructions by 30% (assume all integer instructions take the same time).
  Optimizing the I/O subsystem that reduces the latency of I/O operations from 10 μsec to 5 μsec (that is, speedup of 2).

## Slide 63
Alternative (a):
  Here, F = 0.25 and S = 100 / 70
  Speedup = 1 / (0.75 + 0.25 * 70 / 100) = 1.08
Alternative (b):
  Here, F = 0.40 and S = 2
  Speedup = 1 / (0.60 + 0.40 / 2) = 1.25

## Slide 64: Extension to Multiple Enhancements
Suppose we carry out multiple optimizations to a program:
  Optimization 1 speeds up a fraction F1 of the program by a factor S1
  Optimization 2 speeds up a fraction F2 of the program by a factor S2
1 – F1 – F2
F1
1 – F1 – F2
F1 / S1
F2
F2 / S2
1
(1 – F1 – F2) + F1 / S1 + F2 / S2
Speedup

## Slide 65
In the calculation as shown, it is assumed that F1 and F2 are disjoint.
  S1 and S2 do not apply to the same portion of execution.
If it is not so, we have to treat the overlap as a separate portion of execution and measure its speedup independently.
  F1only , F2only , and F1&2 with speedups S1only , S2only , and S1&2
1 – F1only – F2only – F1&2
F1only
1 – F1only – F2only – F1&2
F1only / S1only
F2only
F2only / S2only
F1&2
F1&2 / S1&2
1
(1 – F1only – F2only – F1&2) + F1only / S1only + F2only / S2only + F1&2 / S1&2
Speedup =

## Slide 66
General expression:
  Assume m enhancements of fractions F1, F2, …, Fm by factors of S1, S2, …, Sm respectively.

## Slide 67: Example 6
Consider an example of memory system.
  Main memory and a fast memory called cache memory.
  Frequently used parts of program/data are kept in cache memory.
  Use of the cache memory speeds up memory accesses by a factor of 8.
  Without the cache, memory operations consume a fraction 0.40 of the total execution time.
  Estimate the speedup.
Main Memory
Cache Memory
CPU
1
(1 – F) + F / S
Speedup =
1
(1 – 0.4) + 0.4 / 8
=
Solution

## Slide 68: Example 7
Now we consider two levels of cache memory, L1-cache and L2-cache.
Assumptions:
  Without the cache, memory operations take 30% of execution time.
  The L1-cache speeds up 80% of memory operations by a factor of 4.
  The L2-cache speeds up 50% of the remaining 20% memory operations by a factor of 2.
We want to find out the overall speedup.

## Slide 69
Solution:
  Memory operations = 0.3
  FL1 = 0.3 * 0.8 = 0.24
  SL1 = 4
  FL2 = 0.3 * (1 – 0.8) * 0.5 = 0.03
  SL2 = 2
1
(1 – FL1 – FL2) + FL1 / SL1 + FL2 / SL2
Speedup
1
(1 – 0.24 – 0.03) + 0.24 / 4 + 0.03 / 2
= 1.24