## Slide 1
Computer Organization and Architecture
Module 5
Prof. Indranil Sengupta
Dr. Sarani Bhattacharya
Department of Computer Science and Engineering
IIT Kharagpur

## Slide 2: Computer Arithmetic

## Slide 3: Introduction
Computers are built using tiny electronic switches.
  Typically made up of MOS transistors.
  The state of the switches are typically expressed in binary (ON/OFF).
To design arithmetic circuits for use in computers, we need to work with binary numbers.
  How to carry out various arithmetic operations in binary?
  How to implement them efficiently in hardware?

## Slide 4: Addition / Subtraction

## Slide 5: Addition of Two Binary Digits (Bits)
When two bits A and B are added, a sum (S) and carry (C) are generated as per the following truth table:
Inputs |  | Outputs | 
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 + 0 = 00
0 + 1 = 01
1 + 0 = 01
1 + 1 = 10
S = A’.B + A.B’ = A  B
C = A.B
HALF ADDER
HA
C
S
B
A

## Slide 6: Addition of Multi-bit Binary Numbers
0 0 1 0 1 1 0
0 1 0 1 0 1 1
+ 0 0 0 1 0 0 1
0 1 1 0 1 0 0
Number A
Number B
Sum S
Carry
1 1 1 1 1 1 0
0 1 1 1 1 1 1
+ 0 0 0 0 0 0 1
1 0 0 0 0 0 0
Number A
Number B
Sum S
Carry
At every bit position (stage), we require to add 3 bits:
  1 bit for number A
  1 bit for number B
  1 carry bit coming from the previous stage
WE NEED A FULL ADDER

## Slide 7
FA
Cout
S
Cin
B
A
Inputs |  |  | Outputs | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Full Adder
S = A’.B’.Cin + A’.B.Cin’ + A.B’Cin’ + A.B.C
= A  B  Cin
Cout = B.Cin + A.Cin + A.B + A.B.Cin
= A.B + B.Cin + A.Cin

## Slide 8: Various Implementations of Full Adder
HALF
ADDER
S
C
B
A
HALF
ADDER
S
C
B
A
OR
A
B
Cin
S
Cout

## Slide 9
Delay of a full adder:
  Assume that the delay of all basic gates (AND, OR, NAND, NOR, NOT) is δ.
  Delay for Carry = 2δ
  Delay for Sum = 3δ
    (AND-OR delay plus one inverter delay)

## Slide 10: Parallel Adder Design
We shall look at the various designs of n-bit parallel adder.
  Ripple carry adder
  Carry look-ahead adder
  Carry save adder
  Carry select adder

## Slide 11: Ripple Carry Adder
Cascade n full adders to create a n-bit parallel adder.
Carry output from stage-i propagates as the carry input to stage-(i+1).
In the worst-case, carry ripples through all the stages.
1 1 1 1 1 1 0
0 1 1 1 1 1 1
+ 0 0 0 0 0 0 1
1 0 0 0 0 0 0
Number A
Number B
Sum S
Carry

## Slide 12
FA0
C0
S0
B0
A0
FA1
C1
S1
B1
A1
FA2
C2
S2
B2
A2
FAn-1
Cn-1
Sn-1
Bn-1
An-1
C3
……
Cn
Two numbers: An-1…A2A1A0 and Bn-1…B2B1B0
Input carry: C0
Sum: Sn-1…S2S1S0
Output carry: Cn
Delay for C1 = 2δ
Delay for C2 = 4δ
Delay for Cn-1 = 2(n-1)δ
Delay for Cn = 2nδ
Delay for S0 = 3δ
Delay for S1 = 2δ + 3δ = 5δ
Delay for S2 = 4δ + 3δ = 7δ
Delay for Sn-1 = 2(n-1)δ + 3δ = (2n+1) δ
Delay is proportional to n

## Slide 13: How to Design a Parallel Subtractor?
Observation:
  Computing A-B is the same as adding the 2’s complement of B to A.
  2’s complement is equal to 1’s complement plus 1.
  Let Xi = Bi’.
FA0
C0 = 1
S0
X0
A0
FA1
C1
S1
X1
A1
FA2
C2
S2
X2
A2
FAn-1
Cn-1
Sn-1
Xn-1
An-1
C3
……
Cn

## Slide 14: A Parallel Adder/Subtractor
n-bit Parallel Adder
A0
A1
An-1
xor
B0
xor
B1
xor
Bn-1
C0
Cn
S0
S1
Sn-1
S2
…
…
…
ADD’ / SUB
xor gate is a controlled inverter

## Slide 15: Carry Look-ahead Adder
The propagation delay of an n-bit ripple carry order has been seen to be proportional to n.
  Due to the rippling effect of carry sequentially from one stage to the next.
One possible way to speedup the addition.
  Generate the carry signals for the various stages in parallel.
  Time complexity reduces from O(n) to O(1).
  Hardware complexity increases rapidly with n.

## Slide 16
Consider the i-th stage in the addition process.
We define the carry generate and carry propagate functions as:
  Gi = Ai.Bi
  Pi = Ai  Bi
Gi = 1 represents the condition when a carry is generated in stage-i independent of the other stages.
Pi = 1 represents the condition when an input carry Ci will be propagated to the output carry Ci+1.
FA
Ci+1
Si
Ci
Bi
Ai
Ci+1 = Gi + Pi.Ci

## Slide 17: Unrolling the Recurrence
Ci+1 = Gi + PiCi = Gi + Pi (Gi-1 + Pi-1Ci-1) = Gi + PiGi-1 + PiPi-1Ci-1
= Gi + PiGi-1 + PiPi-1 (Gi-2 + Pi-2Ci-2)
= Gi + PiGi-1 + PiPi-1 Gi-2 + PiPi-1Pi-2Ci-2 = …..
Ci+1 = Gi +  Gk  Pj + C0  Pj
k=0
i-1
j=0
j=k+1
i
i

## Slide 18: Design of 4-bit CLA Adder
C4 = G3 + G2P3 + G1P2P3 + G0P1P2P3 + C0P0P1P2P3
C3 = G2 + G1P2 + G0P1P2 + C0P0P1P2
C2 = G1 + G0P1 + C0P0P1
C1 = G0 + C0P0
S0 = A0  B0  C0 = P0  C0
S1 = P1  C1
S2 = P2  C2
S3 = P3  C3
4 XOR2 gates
4 AND2 gates
3 AND3 gates
2 AND4 gates
1 AND5 gate
1 OR2, 1 OR3, 1 OR4 and 1 OR5 gate

## Slide 19: Design of 4-bit CLA Adder
C4 = G3 + G2P3 + G1P2P3 + G0P1P2P3 + C0P0P1P2P3
C3 = G2 + G1P2 + G0P1P2 + C0P0P1P2
C2 = G1 + G0P1 + C0P0P1
C1 = G0 + C0P0
S0 = A0  B0  C0 = P0  C0
S1 = P1  C1
S2 = P2  C2
S3 = P3  C3
4 XOR2 gates
4 AND2 gates
3 AND3 gates
2 AND4 gates
1 AND5 gate
1 OR2, 1 OR3, 1 OR4 and 1 OR5 gate

## Slide 20: Design of 4-bit CLA Adder
C4 = G3 + C3P3
C3 = G2 + G1P2 + G0P1P2 + C0P0P1P2
C2 = G1 + G0P1 + C0P0P1
C1 = G0 + C0P0
S0 = A0  B0  C0 = P0  C0
S1 = P1  C1
S2 = P2  C2
S3 = P3  C3
4 XOR2 gates
4 AND2 gates
2 AND3 gates
1 AND4 gates
1 AND5 gate
1 OR2, 1 OR3, 1 OR4 and 1 OR2 gate

## Slide 21: The 4-bit CLA Circuit
C4
C3
C2
C1
C0
G0
P0
G1
P1
G2
P2
G3
P3

## Slide 22
4-bit Carry Look Ahead Circuit
Gi and Pi Generator
A0
B0
A1
B1
A3
B3
A2
B2
P0
G3
G2
G1
G0
P3
P2
P1
xor
xor
xor
xor
S0
S1
S2
S3
C0
C1
C2
C3
C4
3δ
2δ
3δ

## Slide 23: 16-bit Adder Using 4-bit CLA Modules
4-bit CLA Adder
A11-A8
S11-S8
B11-B8
4-bit CLA Adder
A3-A0
S3-S0
B3-B0
C0
4-bit CLA Adder
A7-A4
S7-S4
B7-B4
4-bit CLA Adder
A15-A12
S15-S12
B15-B12
C4
C8
C12
C16
Problem: Carry propagation between modules still slows down the adder

## Slide 24
Solution:
  Use a second level of carry look-ahead mechanism to generate the input carries to the CLA blocks in parallel.
  The second level of CLA generates C4, C8, C12 and C16 in parallel with two gate delays (2δ).
  For larger values of n, more CLA levels can be added.
Delay calculation of a 16-bit adder:
  For original single-level CLA: 14δ
  For modified two-level CLA: 10δ

## Slide 25: Delay of a k-bit Adder
n | TCLA | TRCA
4 | 8δ | 9δ
16 | 10δ | 33δ
32 | 12δ | 65δ
64 | 12δ | 129δ
128 | 14δ | 257δ
256 | 14δ | 513δ
TCLA = (6 + 2 log4 n ) δ
TRCA = (2n + 1) δ

## Slide 26: Carry Select Adder
Basically consists of two parallel adders (say, ripple-carry adder) and a multiplexer.
For two given numbers A and B, we carry out addition twice:
  With carry-in as 0
  With carry-in as 1
Once the correct carry-in is known, the correct sum is selected by a multiplexer.

## Slide 27
Basic building block of a carry-select adder, with block size of 4.
For a multi-bit adder, the number of bits in each carry select block can be either uniform or variable.

## Slide 28
Uniform sized adder
A 16-bit carry select adder with a uniform block size of 4 is shown.
The least significant block needs a single adder (since the carry-in is known).
Total delay is 4 full adder delays, plus 3 MUX delays.

## Slide 29
Variable-sized adder
A 16-bit carry select adder with variable block sizes of 2-2-3-4-5 is shown.
Total delay is 2 full adder delays, plus 4 MUX delays.

## Slide 30: Carry Save Adder
Here we add three operands (say, X, Y and Z) together.
For adding multiple numbers, we have to construct a tree of carry save adders.
  Used in combinational multiplier design.
Each carry save adder is simply an independent full adder without carry propagation.
A parallel adder is required only at the last stage.

## Slide 31
An illustrative example:
A set of full adders generate carry and sum bits in parallel
The sum and carry vectors are added later (with proper shifting)

## Slide 32: An n-bit Carry Save Adder
Full Adder
S0
C0
Z0
Y0
X0
Full Adder
S1
C1
Z1
Y1
X1
Full Adder
S2
C2
Z2
Y2
X2
Full Adder
Sn-1
Cn-1
Zn-1
Yn-1
Xn-1
….
The carry input of the full adder is used as the third input

## Slide 33: Adding m Numbers: Some Examples
CSA
Parallel Adder
CSA
CSA
CSA
CSA
CSA
Parallel Adder
Parallel Adder
m = 3
m = 4
CSA
m = 6

## Slide 34: Generating the Status Flags
Many contemporary processors have a flag register that contains the status of the last arithmetic / logic operation.
  Zero (Z): tells whether the result is zero.
    Can be used for both arithmetic and logic operations.
  Sign (S): tells whether the result is positive (=0) or negative (=1).
    Can be used for both arithmetic and logic operations.
  Carry (C): tells whether there has been a carry out of the most significant stage.
    Used only for arithmetic operations.
  Overflow (V): tells whether the result is too large to fit in the target register.
    Used only for arithmetic operations (addition and subtraction).

## Slide 35
A
B
F
ALU
Assume A, B and F are n-bit registers
NOR
Fn-1
F1
F0
Z Flag
…
F
Fn-1
S Flag
…
F
Carry out
C Flag
…
Overflow can occur during addition when the sign of the two operands are the same.
  Sign of the result becomes different from the sign of the operand(s).
  V = An-1.Bn-1.Fn-1’ + An-1’.Bn-1’.Fn-1
  V = Fn-1  Carry_out

## Slide 36
The MIPS architecture does not have any status flags.
Why?
  MIPS ISA is designed for efficient pipeline implementation.
  Several instructions can be in various stages of execution in the pipeline.
  Flag registers result in side effects among instructions.
MIPS stores information about the flags temporarily in a GPR.
slt $t0, $s1, $s2
beq $t0, $zero, Label